## Slide 1
FSE 100
Robot Hardware Assembly Manual
Spring 2016

## Slide 2: Parts List
1- Intel Edison Board
1- Edison Breakout Board
1- Base Shield
1- Robot Base
2- Wheels + Screws
1- Caster Wheel
2- Servos
2- Servo Mounts
1- Breadboard
LOT -Female Jumpers
LOT- Male Jumpers
1- Sonar Sensor
1- LCD Screen
1- Touch Sensor
1- Light Sensor
LOT – 6-32 ½ in
LOT- 6-32 ¾ in
LOT- 6-32 Nut
1- Battery Pack
LOT- M/F Jumpers
Sonar Mount

## Slide 3: Servo Assembly
1. Gather servo and mounts
2. Slide servo into mount
3. Screw in the top hole for the servo
Note: Make sure servos are calibrated prior to installation

## Slide 4: Robot Body Assembly
1. Gather base and Servo mounts
2. Align mounts on the base and
fasten with screw and nuts
3. Gather caster wheel
and hardware
4. Align and fasten Caster
Wheel to base as shown

## Slide 5: Robot Body Assembly cont’d
5. Here is a picture of the base will all parts on the bottom
At this point, set aside your robot body in a safe place and proceed
to the next set of instructions on how to assemble your Intel
Edison board and its sensors.

## Slide 6: Edison Board/Shield Assembly
1. Gather Edison, breakout
board, and nuts
2. Gently push Edison onto corner
of breakout board
3. Gather breakout board and
spacer hardware
4. Place screws as shown through
top of board and screw on spacers
5. Gather base shield
6. Align pins on shield to ports on
Edison. Gently push down
NOTE: You will feel the board secure into place.
After that, gently tighten the nuts to hold it.
NOTE: If shield doesn’t push down, don’t force it. Make sure you have the shield lined up correctly with the board and push until pins are completely inside the ports..
The screw should go up through the robot base with the nut on the top side of the robot.
NOTE: Do not over tighten screws, they only need
to be gently snugged against the board.

## Slide 7: Sensor Assembly
1. Gather sonar sensor and
4- male/Female jumpers
2. Connect a wire to each output pin
3. Gather LCD and female jumper.
Plug jumper into port on LCD
4. Repeat step 3 with other sensors
The jumper will line up with the port so if it
won’t go in, try flipping the jumper.

## Slide 8: Sensor Assembly cont’d
5. Gather LCD and Edison board
6. Plug LCD into I2C port
7. Plug switch signal into
Digital pin 7 (If provided)
8. Plug sonar sensors outputs as follows:
Echo pin in Digital pin 5
Trigger pin in Digital pin 6
Note: For all sensors, servos, and other electronics: Connect RED wire (power) to the power side of the breadboard. Connect BLACK (Ground) to the ground side of the breadboard. The next steps only refer to the signal pins (White).

## Slide 9: Sensor Assembly cont’d
9. Gather 2- female jumpers,
6- male jumpers, and base
11. Gather Edison board and
robot base
12. Attach Edison board to base by
tightening screws into spacers
13. Plug left servo signal into digital port 3
and right signal into digital port 4
10. Use male jumpers to extend
length of servo cables
MIND THE COLORS: Black to black, red to red,
servo white to female yellow.
This is a bottom view of your robot. Make note of
alignment of holes compared to servos.
14. Connect Edison power
OUT (5V) and GND to Breadboard

## Slide 10: Extra: Edison
Note: Edison Board can be attached in either orientation

## Slide 11: Final Assembly
1. Gather robot base, LCD,
Breadboard, and hardware
2. Place breadboard under the Edison
3. Mount LCD Screen to top
4. Attach Sonar mount to front
6. Attach custom wires from
sensor to the breadboard
5. Attach Touch sensor
to front of base

## Slide 12: Final Assembly
7. Connect wires from sonar and touch
sensor to the breadboard and Edison
8. Gather external battery
9. Place battery under the Edison and connect to the microUSB port on the Edison
Congratulations! The hardware is done, now it is time to move
on to programming your robot.
10. Attach Wheels to the servos, and use wheel screw